Gaui 330x	XAircraft X650	Turbo Ace X720

	Puede usar hasta 13 sensores para chequiar actitud de vuelo, altitud, dirección, posición, temperatura, consumo energético,etc.
	2 tipos el G (Fibra de vidrio) y el C (Fibra de carbono).
	Modos de vuelo: Hover y Cruise.
	Estilo de vuelo: Plus y Cross
	Software de configuración incluido.
	G:1100g; C:950g no incluye batería ni receptor
	Payload: G:700g; C:850g
	Peso máx total: 1800g
	Vuela 12 min con batería de 3300mAh y payload < 1500g
	4 propulsores de 12-inch 60-pitch
	Tiene algoritmos de control de vuelo incorporados que hacen q sea mas facil volarlo (esto es para el control remoto supongo)
	Las hélices impulsadas por motor tienen una eficiencia de 9g/W bajo carga nominal
	Cada grupo hélice-motor proporciona un empuje de 700g
	Unidad de control y unidad de control de entradas y salidas
	ESC-A4 Electric Control Device
	Dispositivo de control de 4 velocidades diseñado todo en 1.
	60 MOS capaces de soportar altas corrientes, ofrece 35 A a la salida con una batería 3s, 5A de capacidad de salida.
	Soporta protocolos UltraPWM y control de frecuencia hasta 500Hz
	Software:
	Diagrama:
	Carbon Fiber Version:In stock / 1 x X650 Fuselage Frame(Carbon Fiber and CNC Aluminum Alloy, 850g) 1 x X650 Body Cover 1 x X650 Landing Gear(Carbon Fiber and CNC Aluminum Alloy) 4 x Outer Rotor Brushless Electric Motor 2 x 12-inch high-strength propeller (positive) 2 x 12-inch high-strength propeller (anti) 1 x XAircraft FC1212-S Flight Controller 1 x XAircraft AHRS-S Attitude Sensor 1 x X650 ESC-A4 High-Speed (UltraPWM) Electric Speed Control Device 1 x XAircraft USB-Link PC Connector x1 1 x Flight Control Management(Parameter Adjustment) Software One year free updates of flight control management software and firmware 8 hours X 5days Email technical support Three-month free warranty for circuit components(No include ESC-A4)
	GPS Module: Pre-sale 1 x GPS Module: Contains a barometer (altimeter), X650 can locate at settled high, fixed or GoHome (required use with electronic compass). 1 x GPS Antenna
	Electronic compass:Pre-sale / 1 x 3-axis electronic compass: Work with GPS Module
	Note: The transmitter,receiver and battery are NOT INCLUDED, you need to prepare a 6-chn(at least) transmitter, a 6-chn(at least) receiver, 3S 2200mAh~5500mAh or 4S 2200mAh~5500mAh lithium battery(instant discharge capacity>15C) and assemble X650 youself.
	El de fibra de carbono: U$S 650 / El de fibra de vidrio: U$S 570 / No incluyen ni batería ni transmisor